## Slide 1: Final year project progress presentation
Wes Gaunt
11 December 2019

## Slide 2: Time domain 0.18µm CMOS analogue MAC for neural networks
Previous work (Matt & ARM)
‘Psuedo’ CMOS
Coming up…
What?
Why?
How?

## Slide 3: Time domain 0.18µm CMOS analogue MAC for neural networks
Multiply ACcumulate operation
Single neuron performs the operation:
      y = XW + b
X and W are vectors of length n.
y and b is are scalars

## Slide 4: Time domain 0.18µm CMOS analogue MAC for neural networks
Inputs are scaled using pulse width.
Long pulse = high magnitude (of x)
Short pulse = low magnitude

## Slide 5: Time domain current to voltage?
Capacitor
CURRENT (mode) x TIME (domain) = (change in) CHARGE
@t = 0. Vcap = VDD/2 = 0.9V

## Slide 6: 2 input neuron example (no offset)

## Slide 7: How?
Conventional CMOS (TSMC 180nm)
Binary weighted (W) current mirror (X)
Leads to W.X…

## Slide 8: First current mirror
Binary weighted ->
4 bits = 0..15
LSB = 0.067
Current mirror ->
NMOS version

## Slide 9: Time domain output
Need output mirror to ‘reset’ the capacitor.

## Slide 10: Complementary (CMOS) mirrors (1)
PMOS

## Slide 11: Complementary (CMOS) mirrors (2)
PMOS source current, VCAP increases.
NMOS sink current, VCAP decreases.

## Slide 12: Preliminary results
200 pairs of inputs.
1 pair of weights for each set of 200 inputs.
Binary output: >= 0.9V?
Compared with MATLAB results.
Voltage domain
100% accuracy
Low resolution issues.

## Slide 13: Next steps
More inputs
b input
Handle negative inputs and weights
Time domain output
Time domain weighting: time x capacitor x VCCS:

## Slide 14: Questions, queries & concerns